Germany & Austria - June-July 1970

Locomotive builder abbreviations

Bergmann	= Bergmann Elektricitäts Werke AG., Berlin, Germany.

Flor	= Wiener Lokomotivfabrik AG., Wien-Floridsdorf, Austria.

Goldeband	=

Krauss L	= Lokomotivfabrik Krauss & Co., Linz am Donau, Austria.

Krauss M	= Lokomotivfabrik Krauss & Co., München, Germany.

WrN	= AG der Lokomotivfabrik, Wiener Neustadt, Austria.

Zeltweg	= ÖAM Workshops, Zeltweg, Austria.

m	= builders number found on the motion.

b	= builders number found on the boiler.

Locomotive information written in italics is from other sources (previous visits, other visitors, etc.), and was not obtained during these visits.

28/6/1970

WEST GERMANY

EBV, Grube Anna, Alsdorf

Two electric coke ovens locos seen here.

? , Esch

No sign of narrow gauge locos. Standard gauge connection removed and converted into a footpath.

Oberaussem-Fortuna

RBW still in use with standard gauge electric locos. Traces of a former narrow gauge system; about 600mm.

? , Ziegelei Düren

600mm line still in use.

29/6/1970

EBV, Grube Anna, Alsdorf

ANNA N.4	0-8-0T	Hen	25246	1951	D 600

ANNA N.8	0-8-0WT	Hen	24396	1938	ELNA 6

ANNA N.10	0-8-0WT	Schw	9963	1930	ELNA 6

0-8-0T

0-8-0T

EBV, Grube Adolf, Merkstein

ADOLF N.4	0-6-0T	OK	13092	1938

Union Rheinische Braunkohlen Kraftstoff AG., Wesseling

UK 2	0-6-0F	Krupp	2826	1952	Rheinbraun		48t

UK-4	0-6-0F	Jung	10855	1950			46t

Eisenfelder Steinwerke, Rosenheim

Closed.

ESTE-Werksbahn, Elkenroth

Closed and lifted.

Schallex Apparatebau GmbH, Siegen-Eintracht

0-4-0D	Jung	8058	1939	DN233	56ps	14t	OOU

30/6/1970

Preussen-Elektra, Grube Altenburg, Borken

1435mm

50	Bo-BoE 	Hen	22651	1934
			SSW	3032	1934		204kw	40t

52	Bo-BoE	Krupp	3560
			SSW	5818	1957		760kw	70t

T101	Bo-2E * 	OK		1929
			Bergmann	415	1929		176kw	72.5t

T102	Bo-2E * 	OK		1929
			Bergmann	416	1929		176kw	72.5t

T105	Bo-2E * 	OK		1930
			AEG	5310	1930		176kw	72.5t

T106	Bo-2E * 	OK		1930
			AEG	5311	1930		176kw	72.5t

*	Self-propelled hopper wagons. They operate in pairs, with an un-powered hopper wagon in the centre.

900mm

2	Bo-BoE 	Hen	26100	1941
			SSW	3685	1941	Brauns.	480kw	60t

3	Bo-BoE 	Hen	26101	1941
			SSW	3686	1941	Brauns.	480kw	60t

4	Bo-BoE 	Hen	29787	1947
			SSW	5116	1947	EL 4	760kw	75t

6	Bo-BoE 	Hen	25219	1950
			SSW	5127	1950	EL 4	760kw	75t

7	Bo-BoE 	Hen	25220	1950
			SSW	5128	1950	EL 4	760kw	75t

12	Bo-BoE 	Hen	25194	1949
			BBC	5562	1949	EL 4	740kw	75t

63	 4wD 	Deutz	57645	1963	KS 125BS	125ps	16t

72	Bo-BoE 	Hen	26509	1956
			AEG	7486	1956		145ps	30t

2	 4wDR*

*	Tower wagon.

Preussen-Elektra, Schacht Stolzenbach, Borken

600mm?

4wDM	Jung

Johannes Orth & Sohn, Quarzitwerke, Frielendorf-Leimsfeld

740mm

4wDM	Diema

? , stone works, Gensunghen

Closed and lifted: building derelict.

Niederhessische Basaltwerke GmbH, Ostheim

A 600mm gauge system, which may have used steam. Closed and lifted, but building still intact, including the loco shed.

1/7/1970

Ziegelwerk Trisching

This works still has narrow gauge skips, but I could not see if they were still in use.

Grube Cecilia, Schmidgaden

Narrow gauge closed and lifted.

Tonwerk Buchtal, near Schmidgaden

600mm still in use; no locos in sight.

Mathiaszeche, near Schwandorf

Narrow gauge closed and lifted recently.

Bayerische Braunkohlen Industrie AG, Wackersdorf, near Schwandorf

Railway closed and replaced by conveyor belts.

Tongrube PLEWA Werk, Klardorf

600mm(?) - still in existance but very overgrown.

Straubing

Several extensive brick works on the south side of the town with narrow gauge railways (600mm?) and skips.

2/7/1970

AUSTRIA

Wolfsegg-Traunthaler Kohlenwerks AG., Ampflwang

There was an extensive narrow gauge system for carrying pit props and other supplies.

3	0-8-0T 	Flor	9493	1944

4	0-8-0T	WrN	5781	1927				OOU

6	0-8-0T 	Hano	9976	1923

600mm

4wDM							Der

4wDM							Der

4wDM

3/7/1970

Österreichische Bundesforste, Reichraming

750mm system still in use, but I could not see any of the locos.

Österreichische Alpine Montan Gesellschaft (ÖAM), Radmer Mines, near Hieflau

The electric line was still used, but I did not see it operating.

900mm

3/15	0-4-0DM	Demag	2032	1937				OOU

13/15?	0-4-0DM							Der

4wE

4/7/1970

ÖAM, Hüttenwerke Donawitz, Leoben-Donawitz

1435mm

200/1	0-4-0F	Flor	3105	1936

200/7	0-4-0T	KM	17234	1946				OOU

600-2	2-6-2T

790mm

40.2	0-4-0T	Krauss L	5760	1907				OOU

40.7	0-4-0T?							OOU

60.5	0-4-0WT	Krauss	7310	1917				OOU

60.8	0-4-0WT	Krauss	7311	1917				OOU

100.18	0-4-0WT	Krauss M	7596	1919

170.3	0-4-0T 	KM	17833	1951

Spielplatz am Glacis, Leoben

790mm

60.6	0-4-0WT	Krauss L	7216	1916				Pvd

6/7/1970

Schoeller-Bleckmann, Mürzuschlag

Standard gauge steam loco standing outside the shed and narrow gauge diesel at work. There four little 4-wheel coaches in the works.

GKB, Graz

415	4-4-0							OOU	671	0-6-0							OOU

56.3115	2-8-0							OOU

56.3203	2-8-0							OOU

56.3242	2-8-0							OOU

56.3268	2-8-0							OOU

152.1364	2-10-0							Dsm

152.1368	2-10-0

152.4785	2-10-0							OOU

152.6729	2-10-0							Dsm

165.1	      D							OOU

V390.1	0-6-0D	Hen	25266

GKB, Koflach

56.3645	2-8-0

7/7/1970

ÖAM, Direction Fohnsdorf

Coal mine at Dietersdorf connected to another mine at Fohnsdorf by a narrow gauge electric railway, using self-propelled hoper wagons. The wagon was seen shuttling along the line every few minutes.

900mm

Nr.2	 4wE*	Zeltweg	1154	1954

*	Self-propelled hopper wagon.

Steirische Gußstahlwerke, Judenburg

400.1	0-8-0T 	Krauss L	7327	1919

760mm

170.4   LISL	0-4-0T	KM	17834	1951

4wD

ÖAM, Donawitz

790mm

60.4	0-4-0WT	Krauss L	(6969	1914?)

100.3	0-4-0WT 	Krauss L	7599	1918

100.7	0-4-0WT 	Krauss L	7387	1918

100.12	0-4-0WT	Krauss L	6581	1912

100.15	0-4-0WT 	Flor	17611	1947

100.18	0-4-0WT	Krauss M	7596	1919?

ÖAM, Eisenerz

900mm

10/100	 4wE	BBC

7/200	 4wE

2/320	 4wE	BBC/Goldeband	364	1956		320ps

3/320	 4wE	BBC/Goldeband	365	1956		320ps

ÖAM, Radmer

900mm

5/15	 4wD							OOU

4/100	 4wE							OOU

5/900	Bo-BoE 	Flor	3348
			BBC	5240	1940

8/7/1970

Altausee

The salt works still has a very narrow gauge railway underground, coming out at an adit. The was no sign of locos, and it is probably man-powered.

Lahnstein-Offensee

Railway lifted; probably narrow gauge.

Ebensee

There used to be a narrow gauge railway here, on the west side of the valley from Bad Ischl to Ebersee, There was a pile of 600mm gauge track sections, but the line was lifted quite some time ago.

9/7/1970

WEST GERMANY

Unterbiberg

Standard gauge siding into a military camp.

Fish ponds, Ismaning

600mm? system still in use - no sign of locos.

Zengermoos

No sign of railway now.

Massenhausen

Railway closed and lifted.

Dachau Moos

No sign of narrow gauge railway now.

Kieswerk Kissing

Closed and lifted.

Württembergische Eisenbahn-Gesellschaft, Nellingen

T34	Bo-BoDR

10/7/1970

Karl Ludowici, Ziegelei Jockgrim

The wagons are modern steel bogie tippers, but some old 4-wheel wood tipper wagons are dumped near the pits.

500mm

102	0-4-0DM	Deutz	13719	1930

108   FRANZ	 4wD	Gmd	4436	1949

Herrenteich

Railway closed & lifted.

Brühl-Süd

Railway closed and lifted, but some 900mm gauge rails are still imbedded in the main road.

Th. Goldschmidt AG., Mannheim-Rheinau

I	 4wD	Deutz	55466	1953	A6M517R

Neunkircher Eisenwerk AG

53	 6wD	Hen	30922	1965

54	0-6-0D	Hen	26565	1959

71	Bo-BoD	Hen	31071	1965

660mm

D4	0-4-0D 	Deutz	22952	1939

Saarbergwerke AG., Grube Heinitz

Closed and dismantled.

Saarbergwerke AG., Kokerei Reden, Landsweiler-Reden

10	0-6-0T	OK	12899	1937				OOU

35	0-8-0T	KM 	17574	1949

36	0-8-0T	KM	17575	1949

37	0-8-0T	KM 	17576	1949

11/7/1970

Saarbergwerke AG., Kokerei Reden, Landsweiler-Reden

10	0-6-0T	OK	12899	1937				OOU

35	0-8-0T	KM	17574	1949

36	0-8-0T	KM	17575	1949

37	0-8-0T	KM	17576	1949